## Slide 1: SR FET TVS Selection Guide
TVS
The following slide shows how to size the TVS used to clamp the leakage spike across the flyback SR FET during transient operation.

## Slide 2: 1. TVS Voltage Rating Selection Ex. SMAJ90A, SR FET VDS Rating = 150V
VDS Rating (ex. 150V)
TVS Electrical Characteristic
TVS Maximum Clamping Voltage
TVS Reverse Stand off Voltage

## Slide 3: 2. Measure the SR‑FET VDS transient stress to validate the effectiveness of the TVS clamp
SRFET VDS: 135V
SRFET VDS: 135V
VIN = 90VAC
VIN = 265VAC
Example: SR‑FET VDS Stress = 90% at Peak Power Operation

## Slide 4: 3. For reliability verification, measure the following parameters. Each value must be lower than the specified Absolute Maximum Rating. Ex. SMAJ90A

## Slide 5: Example: Measure the TVS Power Dissipation TVS Average Power Dissipation at 90V 28V5.9A Steady State
Parameters | Measurement | Unit
Meaasured Energy (V*I Area) | 1.514 | uJ
Measured Period (T) Per Cycle | 12.790 | us
TVS Power Dissipation(Energy/Period) | 118.374 | mW

## Slide 6: Example: Peak Pulse Power @ 2 ms Pulse Width
Peak Pulse Power Rating at 2 ms pulse width is 300W
Ex. SMAJ90A

## Slide 7: Peak Pulse Power During Peak Transient Load 265VAC 28V
Parameters | Measurement | Unit
Meaasured Energy (V*I Area) | 48.350 | uJ
Measured Period (T) Per Cycle | 7.120 | us
Pulse Power Dissipation(Energy/Period) (2ms) | 6.791 | W
Peak Pulse Power over 2 ms period is 6.79W which is way below TVS Peak Pulse Power Rating of 300W at 2 ms Pulse duration