SPECTRA INNOVATIONS INDIA PVT LTD, BANGALORE-43

Schematic and Transformer Design for 20W PSU Using LNK416EG

Customer:   Neugen Embedded                                                                     Doc No:  SIIEPDKB-1042-0112

Schematic Diagram:

| Transformer Construction: Electrical Diagram: |
| --- |
| Mechanical Diagram: |
| Winding Instruction: |
| Primary Winding (Section 1) |
| Start on pin(s) 3 and wind 36 turns (x 1 filar) of item [5] in 1 layer(s) from left to right. On the final layer, spread the winding evenly across entire bobbin. Finish this winding on pin(s) 2. |
| Add 1 layer of tape, item [3], for insulation. |
| Secondary Winding |
| Start on pin(s) 10,9 and wind 38 turns (x 1 filar) of item [6]. Spread the winding evenly across entire bobbin. Wind in same rotational direction as primary winding. Finish this winding on pin(s) 6,7. |
| Add 3 layers of tape, item [3], for insulation. |
| Bias Winding |
| Start on pin(s) 5 and wind 19 turns (x 1 filar) of item [5]. Wind in same rotational direction as primary winding. Spread the winding evenly across entire bobbin. Finish this winding on pin(s) 4. |
| Add 1 layer of tape, item [3], for insulation. |
| Primary Winding (Section 2) |
| Start on pin(s) 2 and wind 36 turns (x 1 filar) of item [5] in 1 layer(s) from left to right. On the final layer, spread the winding evenly across entire bobbin. Finish this winding on pin(s) 1. |
| Add 3 layers of tape, item [3], for insulation. |
| Core Assembly |
| Assemble and secure core halves. Item [1]. |
| Varnish |
| Dip varnish uniformly in item [4]. Do not vacuum impregnate. |
| Comments: |
| 1. Pins 9 and 10 are electrically shorted to each other on the PCB via a copper trace. |
| 2. Pins 6 and 7 are electrically shorted to each other on the PCB via a copper trace. |
| 3. Use of a grounded flux-band around the core may improve the EMI performance. |
| 4. For non margin wound transformers use triple insulated wire for all secondary windings. |
| Materials: |
| Item | Description |
| [1] | Core: EFD25, NC-2H (Nicera) or Equivalent, gapped for ALG of 184 nH/t² |
| [2] | Bobbin: Generic, 5 pri. + 5 sec. |
| [3] | Barrier Tape: Polyester film [1 mil (25 µm) base thickness], 16.40 mm wide |
| [4] | Varnish |
| [5] | Magnet Wire: 26 AWG, Solderable Double Coated |
| [6] | Magnet Wire: 25 AWG, Solderable Double Coated |
| Electrical Test Specifications: |
| Parameter | Condition | Spec |
| Electrical Strength, VAC | 60 Hz 1 second, from pins 1,2,3,4,5 to pins 6,7,9,10. | 1500 |
| Nominal Primary Inductance, µH | Measured at 1 V pk-pk, typical switching frequency, between pin 1 to pin 3, with all other Windings open. | 941 |
| Tolerance, ±% | Tolerance of Primary Inductance | 10 |
| Maximum Primary Leakage, µH | Measured between Pin 1 to Pin 3, with all other Windings shorted. | 23.5 |